HOLO AUDIO

滄 AZURE

-------------------------------------------------------

Preamp / Headphone Amplifier

User's Guide

# Overview

“沧” Azure is a preamp/headphone amplifier from Holo Audio.

“沧” Azure adopts a fully balanced structure with 4 groups/channels. The left and right channels form a fully balanced structure. Each channel has two independent amplification modules to complete the buffering and amplification functions.

There is a total of eight amplifier modules built into the “沧” Azure and they are fully discrete. The design is able to solve the shortcomings of the transistors, so that its tone can exceed the limits of traditional transistors. It also has both the advantages of tubes and transistors. And the use of a large quantity of transistors makes the linearity of the amplifier superior in every way.

The volume control of “沧” Azure is a fully balanced stepping device controlled by a relay. It has a total of 64 steps, and each step is 1 db volume. The advantage is that the noise is minimal and small, and it can be precisely controlled, even at a low volume the left and right channel will not be biased.

“沧”Azure has three output modes, low-impedance headphone output mode, high-impedance headphone output mode, and line output mode.

# Specification

Analog Input

- Single Ended Input x1

  - Largest Value 12Vpp

  - Impedance 3.9Kohm

- Balanced Input x1

  - Largest Value 24Vpp

  - Impedance 7.8Kohm

Analog Output

- Single Ended Line Output x1

  - Largest Value 16Vpp

  - Impedance 33ohm

- Balance Line Output x1

  - Largest Value 32Vpp

  - Impedance 66ohm

- Headphone Single Ended Output x1

  - Low Resistance Mode - 400mW@32ohm load

  - High Resistance Mode - 180mW@300ohm load

- Headphone Balanced Output x1

  - Low Resistance Mode - 1600mW@32ohm load

  - High Resistance Mode - 720mW@300ohm load

# Front Panel

Output indicator, red light is the low-impedance headphone output, and green light is the high-impedance headphone output. Not lit for line output. Input indicator, red light for single-ended input and green light for balanced input.

# Rear Panel

# Remote Control

# Setting

## Set by remote control

For details, please refer to the Instructions in the remote-control section.

## Set through the multi-function knob on front panel

In the default mode, rotate left and right to set the volume, short press the knob to mute/unmute Press and hold the knob to enter the setting mode. Press and hold the knob again to enter the next setting mode. The order is “IN – Input Settings”, “OUT – Output Settings”, “DISP - Display Brightness Settings”. In the setting mode, rotate left or right to make the corresponding settings.

## Volume Setting

The adjustable volume is 64DB, one step per 1DB. When set to 100, it is the maximum, and when it is set to 36, it is the lowest level.

## Input Settings

SE – Single-Ended Input

BL – Balanced Input

## Output Settings

LINE – Line Output

HPL – Headphone low resistance output，Single-ended and balanced headphone ports on the front panel suitable for headphones below 100 ohms impedance. Low resistance output

HPH – Headphone high resistance output，Single-ended and balanced headphone ports on the front panel for headphones with 100 ohm impedance or more.

## Display brightness setting

Set the brightness of the display, a total of 6 levels/shades. The lowest level is to completely turn of the display.

# Text boxes

Input Indicator

Output Indicator

红色-

Multi-Function Knob

Display

S.E. Headphone Input

Balanced Headphone Input

Signal Output

Signal Input

AC Power Input

Reserved (invalid)

Output Settings

Input Settings

Display Brightness Setting

Volume -

Volume +

Mute